## Slide 1: Core Flight System Software Bus Networking Application Design As Built
Christopher.D.Knight@nasa.gov
(650) 604-3471
NASA Ames Research Center
Intelligent Systems Division (Code TI)

## Slide 2
Design (1)
SBN is a cFS application that…
…connects the local software bus to one or more other cFS nodes (who are also running SBN) such that all messages sent by an application on one bus will be received by an application on another bus.
…has a modular network architecture (TCP, UDP, Serial, SpaceWire, etc.) to connect peers and supports mixed-mode peer networks.
…utilizes an “announce” and “heartbeat” protocol to provide network state awareness to the SBN application.
…remaps and filters outgoing messages (cFS table-configured.)

## Slide 3
Design (2)
SBN is a cFS application that…
…subscribes to the CFE_SB_ALLSUBS_TLM_MID and sends a CFE_SB_SEND_PREV_SUBS_CC to receive all existing subscriptions at startup.
…subscribes to the CFE_SB_ONESUB_TLM_MID message that informs SBN when a local application has (un)subscribed.
…receives messages from peers (either via “select” polling or per-peer task, compile-time configurable) and publishes the messages locally.
…gets messages for peers from the SB (either via “polling” or per-peer task, compile-time configurable) and sends the messages to peers.
...Ensures all SBN and CCSDS headers are big-endian over the wire.

## Slide 4
Concerns/Future Developments
Issue | Fix
Chatty protocol of announcing and heartbeating. Need for all net types? | Some improvements already. Push protocol chatter down to modules?
SBN “star network” only, lacks any forwarding/routing capability. | Develop forwarding/routing architecture, or develop/integrate separate app (CI/TO?)
cFS SB limits the total number of MIDs to 256. Large SBN networks will need significantly more. | Leverage remapping/filtering. Increase SB limits. Investigate impacts.
SBN subscribes to all MIDs of all other subs, plus subs for all peers. | Increase limits, leverage filtering to limit subs for peers.
SBN provides no guarantee of delivery. | Use TCP, or (re)add a guarantee of delivery windowing logic.
SBN connections defined at start time. | Allow for command-driven network configuration?

## Slide 5: Context Diagram
CPU
5
Messages/
Subscriptions
SBN
SB
Peer 2
SBN
SB
Peer 3
SBN
SB
NetNum 1
Peer 1
SBN
SB
NetNum 0
Notes: testnotes

## Slide 6: Sequence: Setup
Ann.
Network
Startup
“announce”
“announce”
timeout
“announce”
“announce”
timeout
“announce”
timeout
<SB messages>
SBN
SB
Peer
“local subs”
Announcing
Heartbeating
Startup
Heartbeating
“here are my subs”
“here are my subs”

## Slide 7: Sequence: Packet Exchange
Subscribe()
“enable sub reporting”
SubscribeLocal()
Unsubscribe()
“subs” from peer
“subs”
<SB messages>
SendMsg()
cFS Apps
cFS Apps
SB
SBN
Peer
…

## Slide 8: Sequence: Teardown
<SBmessages>
<SB messages>
Terminated
SBN_
HEARTBEAT_
TIMEOUT
“announce”
SBN
Announcing
Heartbeating
Heartbeating
“announce”
Network
Peer

## Slide 9: Configuration Files: Module Data
Parameter | Type | Description
Protocol ID | int | The identifying number for this protocol.
Protocol Name | char[50] | The name of this protocol.
Module Path | char[50] | The path to the module file.
Module Operations Symbol | char[50] | The symbol in the module’s symbol table containing the methods the module provides.
The configuration file is modeled on the ES startup script, one record per line, fields separated by commas and lines terminated with semicolons. For example:
1, UDP, /cf/sbn_udp_module.so, SBN_UDP_Ops;
2, TCP, /cf/sbn_tcp_module.so, SBN_TCP_Ops;
6, Serial, /cf/sbn_serial_module.so, SBN_Serial_Ops;

## Slide 10: Configuration Files: Peer Data
Parameter | Type | Description
CPU Name | char[ SBN_MAX_PEERNAME_LENGTH] | The CPU name of the node (needs to match CFE_CPU_NAME.)
CPU ID | uint32 | The ID of the node (needs to match CFE_CPU_ID.)
Protocol ID | int | The protocol ID for the module to connect to this node.
Spacecraft ID | uint32 | The Spacecraft ID
QoS | uint8 | The QoS of the connection.
NetNumber | int | The Network Number (if you have multiple distinct networks sharing peers.)
+++ module-specific parameters (e.g. hostname/port, serial device filename, etc.) |  | 

## Slide 11: Configuration Parameters (1)
Parameter #define SBN_* | Default | Description
int MAX_NETWORK_PEERS | 4 | Number of peers allowed a network.
int SUB_PIPE_DEPTH | 256 | Depth of the subscription pipe.
int MAX_ONESUB_PKTS_ON_PIPE | 256 | Maximum number of individual subscription messages on the subscription pipe.
int MAX_ALLSUBS_PKTS_ON_PIPE | 64 | Maximum number of “all subscriptions” messages on the subscription pipe.
int MAX_INTERFACE_TYPES | 6 | Max number of interface modules that can be loaded.
int SCH_PIPE_DEPTH | 10 | Depth of the scheduler pipe.
int MOD_STATUS_MSG_SIZE | 128 | In Hk messages, the module can provide its own data. This is the max size of that block of RAM.
boolean DEBUG_MSGS | undef | If defined, SBN will produce copious debug events.

## Slide 12: Configuration Parameters (2)
Parameter #define SBN_* | Default | Description
char * VOL_MODULE_FILENAME | “/ram/SbnModuleData.dat” | Path of the module configuration in the volatile memory.
char * NONVOL_MODULE_FILENAME | “/cf/SbnModuleData.dat” | Path of the module configuration in the non-volatile memory.
int MODULE_FILE_LINE_SIZE | 128 | Max length of a module file line.
char * VOL_PEER_FILENAME | “/ram/SbnPeerData.dat” | Path of the peer configuration in the volatile memory.
char * NONVOL_PEER_FILENAME | “/cf/SbnPeerData.dat” | Path of the peer configuration in the non-volatile memory.
int PEER_FILE_LINE_SIZE | 128 | Max length of a peer file line.
boolean SEND_TASK | undef | Use a per-peer task to wait on the peer’s pipe and send messages to the peer as soon as they are read off the pipe. If undef, pipes are polled every time SCH wakes up SBN.
boolean RECV_TASK | undef | Use a per-peer task to wait on the peer’s connection and send messages to the bus as soon as they are received by the peer. If undef, peer connections are polled every time SCH wakes up SBN.

## Slide 13: Commands
Command (#defined as SBN_<cmd>_CC) | Parameters | Description
NOOP | (none) | General app aliveness test – verifies command handler and event generation.
RESET | (none) | Reset application housekeeping telemetry counters.
RESET_PEER | uint8 PeerNum | Resets the task, stopping and clearing config.
SEND_HK | (none) | SBN sends telemetry containing the current status of the SBN network.
MYSUBS | (none) | SBN sends telemetry containing the local subscriptions that SBN is subscribed to.
PEERSUBS | uint8 PeeerNum | SBN sends telemetry containing the subscriptions the local SBN is aware of for that peer.
SCH_WAKEUP | (none) | SBN waits on wakeup messages from the scheduler and also has a built-in timeout in case SCH is not running.
Housekeeping requests are sent as commands with housekeeping-specific command codes. Responses all are sent as telemetry with the same message ID but the first byte of the response is the command code that made the request.

## Slide 14: Housekeeping (1)
14
Telemetry Point | Data Type | Description
TlmHeader | uint8[CFE_SB_TLM_HDR_SIZE] | The CCSDS header.
CC | uint8 | The command code that requested this housekeeping.
<Padding> | uint8 * 3 | 32-bit align the remainder
CmdCount | uint8 | Number of successful ground commands (includes commands from on board sources).
ErrCount | uint8 | Number of commands with process errors.
SubCount | uint16 | Number of subscriptions for local apps.
EntryCount | uint16 | Total number of entries (hosts and peers.)
HostCount | uint16 | Number of host entries.
PeerCount | uint16 | Number of peer entries.
PeerStatus | SBN_PeerStatus_t * SBN_MAX_NETWORK_PEERS | Details for each peer.
SBN_HkPacket_t
Notes: testnotes

## Slide 15: Housekeeping (2)
15
Telemetry Point | Data Type | Description
InUse | uint8 | Set to !0 when in use.
QoS | uint8 | The CCSDS quality of service.
ProtocolId | uint8 | The ID of the protocol to use to connect to this peer.
State | uint8 | Whether this node is connected (heartbeating) or disconnected (announcing.)
Name | char * SBN_MAX_PEERNAME_LENGTH | The name of the peer.
ProcessorId | uint32 | The cFS processor ID of the peer.
SpaceCraftId | uint32 | The ID of the spacecraft for this peer.
LastSent | OS_time_t | Last time I sent this peer a message.
LastReceived | OS_time_t | Last time I received a message from this peer.
SentCount | uint16 | Number of messages sent to this peer since last reset.
RecvCount | uint16 | Number of messages received from this peer since last reset.
SentErrCount | uint16 | Number of errors raised when sending to this peer.
RecvErrCount | uint16 | Number of errors raised when trying to receive from this peer.
SubCount | uint16 | Number of subscriptions sent to me by this peer.
<Padding> | uint8 * 2 | 32-bit align the next block.
IFData | uint8 * 32 | IF-specific private data block.
SBN_PeerStatus_t
Notes: testnotes

## Slide 16: Housekeeping (3)
16
Telemetry Point | Data Type | Description
TlmHeader | uint8[CFE_SB_TLM_HDR_SIZE] | The CCSDS header.
CC | uint8 | The command code that requested this housekeeping.
PeerIdx | uint8 | The index of the peer this is a subscription list for.
SubCount | uint16 | The number of subscriptions for this peer.
Subs | CFE_SB_MsgId_t * SBN_MAX_SUBS_PER_PEER | Subscriptions for this peer.
SBN_HkSubsPacket_t
Notes: testnotes

## Slide 17: Event IDs
Event ID #define SBN_..._EID | Description
SB | Local software bus
INIT | Application initialization
MSG | SB message
FILE | Configuration (module and peer) file
PEER | Local peer resources (pipes, memory)
PROTO | Network protocol
CMD | Commanding
SUB | Subscriptions

## Slide 18: Network Protocol
Field | Type | Description
MsgSize | uint16 | Size of the payload.
Type | uint8 | Announce/Sub/Unsub/App
CpuId | uint32 | CPU ID of the sender. (Needed for UDP).
Field | Type | Description
MsgId | uint16 | Message ID of the subscription.
Qos | uint8 + uint8 | Qos
(Un)Subscription Message
Field | Type | Description
Ident | uchar[48] | GIT identity $Id: <MD5>$
Announce Message

## Slide 19: Network Module API
int Load(const char **, int, void *);
int InitHost(SBN_HostInterface_t *Host);
int InitPeer(SBN_PeerInterface_t *Peer);
int Send(SBN_PeerInterface_t *Peer, SBN_MsgType_t MsgType,
SBN_MsgSize_t MsgSize, SBN_Payload_t *Payload);
int Recv(SBN_PeerInterface_t *Peer, SBN_MsgType_t *MsgTypePtr,
SBN_MsgSize_t *MsgSizePtr, SBN_CpuId_t *CpuIdPtr,
SBN_Payload_t *PayloadBuffer);
int ReportModuleStatus(SBN_ModuleStatusPacket_t *Buffer);
int ResetPeer(SBN_PeerInterface_t *Peer);