## Slide 1: CFS Application - SBN Software Bus Network Services IP Version Current Status Report February 28, 2007
  Robert McGraw
  Code 582/MTI
  robert.j.mcgraw@nasa.gov
  301-286-5069

## Slide 2
SBN - What We Currently Have
  CFS Application for inter-processor communication (SBN no longer embedded in the cFE)
  IP Version Only
  Designed to run on Ethernet, Spacewire, SOIS and 1394 (Firewire) without SBN code changes
  Learns of Peers via Peer Configuration File
  Can be used with cFE Version 4.1.0 or later
  Requires no changes to existing cFE/CFS applications
Notes: This idea is possible, but it would add a significant amount of complexity to an already complex application. Let me explain. It is simple to have a single function for each of these 4 items, but that’s not enough to abstract ( and this has been done in the current version).

## Slide 3
SBN - What We Don’t Have
Quality Of Service not yet in use (but hooks are in)
Cannot Interface to 1553 - may need a separate 1553 version of SBN
There is no way to send large pkts to peers. Currently maximum network packet size is constrained by MTU (usually ~1500 bytes)
Cannot Learn of Peers that are not listed in the Peer Configuration File
Cannot Send Raw Packets (Non IP) to peers
Bridging two subnets is not yet supported (some hooks are in).
Notes: This idea is possible, but it would add a significant amount of complexity to an already complex application. Let me explain. It is simple to have a single function for each of these 4 items, but that’s not enough to abstract ( and this has been done in the current version).

## Slide 4
SBN - Deviation from September Plan
At the September 2006 meeting, we decided to abstract SBN so that the same SBN code can be used with or without IP on Ethernet, Spacewire, 1553, or SOIS. This was to be done by having generic functions for the following:
to initialize an interface (ifinit)
to send a message to any destination (ifsend)
to receive a message from any destination. (ifrcv)
to terminate an interface (ifclose)
This idea is possible, but to try and cover all possibilities with the same SBN would add significant complexity to an already complex application.
It seems to be more feasible to have an IP version of SBN that is separate from the non IP version and possibly a third version that interfaces to 1553.
Notes: This idea is possible, but it would add a significant amount of complexity to an already complex application. Let me explain. It is simple to have a single function for each of these 4 items, but that’s not enough to abstract ( and this has been done in the current version).

## Slide 5: SBN - Configuring the Nodes
To configure each node the user must:
Create the Peer Configuration File:
Define Peer Name, IP Address, Data Port and Protocol Port for each peer.
  CPU1, 192.168.001.004, 15820, 5820;
  CPU2, 192.168.001.006, 15820, 5821;
  CPU3, 192.168.001.008, 15820, 5822;
Each node gets a copy of the same Peer Configuration File
Set values for the following prior to building (if default is insufficient)
SBN_MAIN_LOOP_DELAY, default is 1 second,
SBN_TIMEOUT_CYCLES, default is set to 5
SBN_VOL_PEER_FILENAME, default "/ram/SbnPeerData.dat"
SBN_NONVOL_PEER_FILENAME, default "/cf/SbnPeerData.dat"
SBN_MAX_SUBS_PER_PEER, default 256
Notes: How do you configure the network system
step1:
I think 3 configuration items would cover each option on the previous page - IP or not, and QOS or not, and which drivers.
- needs some input from a makefile expert
step2:
In most systems the configuration on each node is slightly different, but on a spacecraft, verifying correct config files on each node would be painful for the user if they were all slighty different. Identical files would not only simplify verifying the correctness on each node, but it would also provide a simpler way to configure the network.

## Slide 6
SBN - SB Interface
SB
SBN
SBN Subscribes to subscription pkts
SBN Requests current subscriptions via cmd
Turn on Subscription reporting via cmd
SBN uses the following SB API's during normal operation
CFE_SB_CreatePipe(…)
CFE_SB_SubscribeLocal(…)
CFE_SB_SendMsg(…)
CFE_SB_RcvMsg(…)
SB Sends Msg with current
subscriptions
For each call to CFE_SB_Subscribe,
SB sends a msg to SBN with the
msgid, pipe and QOS information
(subscription reporting)

## Slide 7: SBN - Peer Table
  The subscription list in the peer table has two purposes:
  1. allows the routing to be cleaned up whenever a peers heartbeat stops
  2. provides the Qos to the SBN sending the message over the network
Peer 0
Peer Name
Dest Adr
Pipe ID
Subscription 0
“CPU2”
Subscription 1
Subscription 2
Subscription 256
192.168.1.6
10
0x1842
MsgId
Reliability
Priority
0
0
0x1801
0x081A
1
1
0
1
Peer 1
Peer Name
Dest Adr
Pipe ID
Subscription 0
“CPU3”
Subscription 1
Subscription 2
Subscription 256
12
0x0810
MsgId
Reliability
Priority
0
0
0x1865
0
0
Peer tables for the “cpu1” processor
Peer State
Peer State
Heartbeating
Heartbeating
Heartbeat Timer
Heartbeat Timer
3
1
192.168.1.8
Subscription Count
3
Subscription Count
2

## Slide 8: SBN - Network Message Types
SBN uses 7 unique network messages :
ANNOUNCE - Sent on initialization to all peers.
ANNOUNCE ACK - Sent in response to an ANNOUNCE
HEARTBEAT - Sent periodically to all peers
HEARTBEAT ACK - Sent in response to HEARTBEAT
SUBSCRIBE - Sent to all peers when a task subscribes to a message
      (via CFE_SB_Subscribe)
UNSUBSCRIBE - Sent to all peers when a task unsubscribes to a message
        (via CFE_SB_Unsubscribe)
APP MESSAGE - Sent to all subscribing peers when a message is read from a pipe

## Slide 9: SBN - Network Message Formats
SBN appends a custom header to each network message so that
the message type and the sender are easily identified by the
receiving SBN
 | uint32 Msg Type | 8-byte string | Number of bits are shown in parenthesis
ANNOUNCE | 0x10 | Sender | Unused
ANNOUNCE ACK | 0x11 | Sender | Unused
HEARTBACK | 0x20 | Sender | Unused
HEARTBEAT ACK | 0x21 | Sender | Unused
SUBSCRIBE | 0x30 | Sender | MsgId (16) ¦ QOS-Reliability (8) ¦ QOS – Priority (8)
UNSUBSCRIBE | 0x40 | Sender | MsgId (16) ¦ QOS-Reliability (8) ¦ QOS – Priority (8)
APP MSG | 0x50 | Sender | Variable lenght
SBN HDR
SBN DATA PORTION

## Slide 10: SBN – Announce Message Processing
Announce Message from peers
Network Side
SBN
Announce Ack from Peer
Immediately send
an Announce Ack
back to sender
Set “Announce
Ack Received”
flag for peer
Announce Ack to Peer
Announce message to all peers
Initialization
Send another Announce Msg to Peer
Check “Announce
Ack Received”
flag every TO
period, if not set...

## Slide 11: SBN – Heartbeat Message Processing
Heartbeat Message from peers
Network Side
SBN
Heartbeat Ack from peer
Immediately send
an Heartbeat Ack
back to sender
Set “Heartbeat
Ack Received”
flag for peer
Heartbeat Ack to peer
Send Heartbeat Msg to Peer
Check “Announce
Ack Received”
flag every TO
period, if set...
Send another heartbeat msg to peer (normal case)
For each peer...
Check “Heartbeat
Ack Received”
flag every TO
period, if set...

## Slide 12: SBN – Data Port Message Processing
Subscriptions from peers
Network Side
SB side
SBN
App Msgs from peers
Subscriptions from
Local Apps
Subscription to all “heartbeating” peers
Add to local
subscription
list
App Msgs to Peer 1
Subscription Pipe
Peer 1 Pipe
Add to senders
subscription
list
Call SB API
CFE_SB_SubscribeLocal
MsgId from network msg,
Senders pipe
Strip SBN Hdr
('App Msg' Id &
sender name)
Call SB API
CFE_SB_SendMsg
App Msgs to Peer 2
Peer 2 Pipe
Add SBN Hdr
('App Msg' Id &
this peer name)
Add SBN Hdr
('App Msg' Id &
this peer name)
App Msg to peer 1
App Msg to peer 2

## Slide 13: SBN – PDL Page 1
  SBN Task Main
Initialization
Create Subscription Pipe
Send Cmd to SB to turn on subscription reporting
Request a list of previous subscriptions from SB
Create Cmd Pipe
Loop Through Peers listed in configuration file
if (entry == self)
Create protocol socket
bind protocol socket to prtotocol port listed in file
Create data socket
bind data socket to data port listed in file
else
Create Pipe for peer. (Enter Pipe Id in Channel Tbl)
Create Socket for peer. (Enter socket Id in Channel Tbl)
Send ANNOUNCE Msg to peer
End Loop Through Entries in configuration file
End Initialization
Forever
Wait 1sec (wait time is a configurable parameter)
Check for Incoming Network Messages (see next page for more detail)
RunProtocol (see pdl page 3 for more detail)
Check Subscription Pipe (see pdl page 4 for more detail)
Check Peer Pipes (see pdl page 4 for more detail)
Check Cmd Pipe (see pdl page 4 for more detail)
End Forever
End SBN Task Main

## Slide 14: SBN – PDL Page 2
  SBN Task Main
Initialization
Forever
Wait 1sec (wait time is a configurable parameter)
Check for Incoming Network Messages
If ANNOUNCE, find sender, send ANNOUNCE ACK back
  If ANNOUNCE ACK, find sender, set “announce ack rcvd flag” for sender
  If HEARTBEAT, find sender, send HEARTBEAT ACK back
  If HEARTBEAT ACK, find sender, set “heartbeat ack rcvd flag” for sender
  If SUBSCRIBE,
  find sender
  log subscription in peer's subscription list
  call CFE_SB_SubscribeLocal, give MsgId from network msg and PipeId from peer table,
  If UNSUBSCRIBE,
  find sender
  remove subscription from peer's subscription list
  call CFE_SB_UnsubscribeLocal, give MsgId from network msg and PipeId from peer table,
  If APP MSG, strip SBN Hdr (APP MSG identifier) and send message to SB for routing (via CFE_SB_SendMsg)
End Check for Incoming Network Messages
RunProtocol
Check Subscription Pipe
Check Peer Pipes for SB Message
Check Command Pipe for Message
End Forever
End SBN Task Main

## Slide 15: SBN – PDL Page 3
  SBN Task Main
Initialization
Forever
Wait 1sec (wait time is a configurable parameter)
Check for Incoming Network Messages
RunProtocol
Loop Through Peers
peer timer++
if peer timer >= timeout_cycles (cfg param, default = 5)
reset timer
if peer state == ANNOUNCING
if “announce ack rcvd flag” is set
change peer state to HEARTBEATING
send local subscriptions to peer
send heartbeat message to peer
else if “announce ack rcvd flag” not set
send another announce message to peer
end if announce ack rcvd flag...
else if peer state == HEARTBEATING
if “heartbeat ack rcvd flag” is set
send another heartbeat message to peer
else if “heartbeat ack rcvd flag” is not set
change state back to ANNOUNCING
send “heartbeat lost” event
unsubscribe to all subscriptions from peer
send announce message to peer
end if heartbeat ack rcvd flag..
end if peer state ....
end if peer timer...
end loop through peers
End RunProtocol
Check Subscription Pipe
Check Peer Pipes for SB Message
Check Command Pipe for Message
End Forever
End SBN Task Main

## Slide 16: SBN – PDL Page 4
  SBN Task Main
Initialization
Forever
Wait 1sec (wait time is a configurable parameter)
Check for Incoming Network Messages
RunProtocol
Check Subscription Pipe (for local subscribes and unsubscribes)
If Subscription found
Log subscription in local subscription list
Add SUBSCRIPTION identifier and send to all peers w/ state = HEARTBEATING
If Unsubscription found
Remove subscription from local subscription list
Add UNSUBSCRIPTION identifier and send to all peers w/ state = HEARTBEATING
end Check Subscription Pipe
Check Peer Pipes for SB Message
Loop Through Peers w/ state = HEARTBEATING
If Message found
Add APP MSG identifier and send to proper network peer
end Check Peer Pipes
Check Command Pipe for Message
If Request for HK, Send HK Msg
If Ground Command, Process Ground Command
end Check Command Pipe
End Forever
End SBN Task Main

## Slide 17: SBN - Resets
Power-On and Processor Resets:
  All connections with peers are terminated.
  All subscriptions are lost and need to be recreated during initialization.

## Slide 18: SBN – Commands
Sets wait time in milliseconds
Sends Single Peer info in event
Sets heartbeat timeout in # of forever loop cycles
Description
Parameters
Function
Code
Command
Sends network diagnostic information in packet
Reset command execution counter and command error counters to zero
None
Reset Counters
Increments command execution counter
None
No-op
Writes all ram peer information to telemetry file
Send All Peer Info
Send Single Peer Info
Set forever loop wait time
Set heartbeat timeout cycles
Send Network Diagnostic pkt
None
peer name
wait time in mS
Timeout cycles
None
0x2
0x3
0x1
0x4
0x5
0x6
0x7

## Slide 19: SBN - Telemetry
Command Counter
Command Error Counter
Names of Peers
State of Peers
Count of pkts sent to each peer
Count of pkts recvd from each peer
Count of local subscriptions
Count of subscriptions received by each peer

## Slide 20: SBN – Error Event Messages
Error Event Messages
  SBN APP Will Terminate, Peer File Not Found or Data Invalid!
  SBN APP Will Terminate, Error Creating Interfaces!
  SBN APP Initialized V1.0, AppId=%d
  "%s:Peer file %s failed to open", CFE_CPU_NAME,Nonvolatile Filename
  "%s:Invalid SBN peer file line,exp %d items,found %d"
  "%s:Error copying file data for %s,status=0x%x"
  "%s:Error creating pipe for %s,status=0x%x"
  "%s:socket call failed,line %d,rtn val %d,errno=%d"
  "%s:bind call failed,line %d,rtn val %d,errno=%d"
  "%s:Unexpected state(%d) in SBN_RunProtocol for %s"
  "%s:Error recving network message, srcName %s invalid"
  "%s:Cannot process subscription from %s,max(%d)met."
  "%s:Error sending %s to %s stat=%d"

## Slide 21: SBN – Informational Event Messages
Informational Event Messages
  “SBN APP Initialized V1.0, AppId=%d”
  "%s:Peer file %s failed to open", CFE_CPU_NAME,Volatile Filename
  "%s:Opened SBN Peer Data file %s"
  "%s:Pipe %s created"
  "%s:%s Alive, changing state to SBN_HEARTBEATING"
  "%s:%s Heartbeat lost, changing state to SBN_ANNOUNCING"
  "%s:AppMsg 0x%04X,sz=%d destined for %s truncated to %d(max sz)"
  "%s:Error sending subs to %s,LclSubCnt=%d,max=%d"
  "%s:UnSubscribed %d MsgIds from %s"

## Slide 22: SBN – Subscription Example (1 of 2)
CPU3
(Local Subscriptions not shown)
In the following slides, P#’s refer to pipes and A#’s refer to applications.
1. A1 subscribes to MsgId 10 on Pipe 3 (P3) with QOS of 0,0 (meaning low reliability, low priority).
2. SB1 does the following:
a. Updates ‘CPU1’ SB routing tables with MsgId 10 to Pipe 3.
b. Sends a message to SBN1 with subscription details (subscription report)
3. SBN1 does the following after receiving the subscription report:
a. Adds subscription to “Local Subscription” list
b. Sends a “SUBSCRIBE” network message to all “heartbeating” peers
SB1
SBN1
A2
A1
CPU1
Pipe 3
(P3)
P1
(cpu2)
P4
P2
(cpu3)
SB3
SBN3
A6
A5
P11
P9
(cpu1)
P12
P10
(cpu2)
SB Routing
Table
MsgId
Pipe
MsgId
Pipe
SB Routing Table
10
3
SUBSCRIBE MSG from cpu1, MsgId 10, Qos0,0
MsgId
Peer 0
Peer 1
QOS
“CPU2”
state
Local Subscriptions
count
MsgId
QOS
10
0,0
pipe 1
timer
ack rcvd flags
sub count
in use flag
MsgId
“CPU3”
state
QOS
pipe 2
timer
ack rcvd flags
sub count
in use flag
SB2
SBN2
A4
A3
CPU2
P7
P5
(cpu1)
P8
P6
(cpu3)
SB Routing
Table
MsgId
Pipe
MsgId
Peer 0
Peer 1
QOS
“CPU1”
state
Local Subscriptions
count
MsgId
QOS
pipe 5
timer
ack rcvd flags
sub count
in use flag
MsgId
“CPU3”
state
QOS
pipe 6
timer
ack rcvd flags
sub count
in use flag
MsgId
Peer 0
“CPU1”
state
QOS
pipe 9
timer
ack rcvd flags
sub count
in use flag
MsgId
Peer 1
“CPU2”
state
QOS
pipe 10
timer
ack rcvd flags
sub count
in use flag
SUBSCRIBE MSG from cpu1, MsgId 10, Qos0,0
Ethernet

## Slide 23: SBN – Subscription Example (2 of 2)
CPU3
(Local Subscriptions not shown)
SB1
SBN1
A2
A1
CPU1
Pipe 3
(P3)
P1
(cpu2)
P4
P2
(cpu3)
SB3
SBN3
A4
A3
P11
P9
(cpu1)
P12
P10
(cpu2)
SB Routing
Table
MsgId
Pipe
MsgId
Pipe
SB Routing Table
10
3
SUBSCRIBE MSG from cpu1, MsgId 10, Qos0,0
MsgId
Peer 0
Peer 1
QOS
“CPU2”
state
Local Subscriptions
count
MsgId
QOS
10
0,0
pipe 1
timer
ack rcvd flags
sub count
in use flag
MsgId
“CPU3”
state
QOS
pipe 2
timer
ack rcvd flags
sub count
in use flag
SB2
SBN2
A4
A3
CPU2
P7
P5
(cpu1)
P8
P6
(cpu3)
SB Routing
Table
MsgId
Pipe
10
5
MsgId
Peer 0
Peer 1
QOS
“CPU1”
state
Local Subscriptions
count
MsgId
QOS
pipe 5
timer
ack rcvd flags
sub count
in use flag
MsgId
“CPU3”
state
QOS
pipe 6
timer
ack rcvd flags
sub count
in use flag
MsgId
Peer 0
“CPU1”
state
QOS
pipe 9
timer
ack rcvd flags
sub count
in use flag
MsgId
Peer 1
“CPU2”
state
QOS
pipe 10
timer
ack rcvd flags
sub count
in use flag
10
0,0
Ethernet
In response to the network ‘SUBSCRIBE’ message, SBN2 will :
Find the sender of the message (cpu1)
Look up the pipe number for the sender in the channel table (5)
Do a CFE_SB_SubscribeLocal of msgId 10, on cpu1 pipe.(5)
Add the MsgId and QOS to its subscription list for CPU1.
SBN3 will respond to the SUBSCRIBE message in the same way.
SUBSCRIBE MSG from cpu1, MsgId 10, Qos0,0
10
0,0
10
9

## Slide 24: SBN – Message Send Example
CPU3
(Local Subscriptions not shown)
SB1
SBN1
A2
A1
CPU1
Pipe 3
(P3)
P1
(cpu2)
P4
P2
(cpu3)
SB3
SBN3
A4
A3
P11
P9
(cpu1)
P12
P10
(cpu2)
SB Routing
Table
MsgId
Pipe
MsgId
Pipe
SB Routing Table
10
3
MsgId
Peer 0
Peer 1
QOS
“CPU2”
state
Local Subscriptions
count
MsgId
QOS
10
0,0
pipe 1
timer
ack rcvd flags
sub count
in use flag
MsgId
“CPU3”
state
QOS
pipe 2
timer
ack rcvd flags
sub count
in use flag
SB2
SBN2
A4
A3
CPU2
P7
P5
(cpu1)
P8
P6
(cpu3)
SB Routing
Table
MsgId
Pipe
10
5
MsgId
Peer 0
Peer 1
QOS
“CPU1”
state
Local Subscriptions
count
MsgId
QOS
pipe 5
timer
ack rcvd flags
sub count
in use flag
MsgId
“CPU3”
state
QOS
pipe 6
timer
ack rcvd flags
sub count
in use flag
MsgId
Peer 0
“CPU1”
state
QOS
pipe 9
timer
ack rcvd flags
sub count
in use flag
MsgId
Peer 1
“CPU2”
state
QOS
pipe 10
timer
ack rcvd flags
sub count
in use flag
10
0,0
Ethernet
10
0,0
10
9
Application A3 sends a message with message ID 10.
SB routes the message to pipe 5.
SBN2 reads the message off pipe 5, adds the SBN Hdr (APP MSG identifier and Src Name=CPU2),
then sends it to CPU1. (All pipe 5 pkts go to CPU1)
SBN1 reads the message off the network, strips the APP MSG identifier and sends it to SB for routing.
Inside the CFE_SB_SendMsg API, the message is routed to pipe 3.
Application A1 receives the message via the CFE_SB_RcvMsg API.
CFE_SB_SendMsg
CFE_SB_SendMsg

## Slide 25
SBN – for reference
SBN
calls socket,sendto,
recvfrom & SB APIs
OS
cFE Demo, 2004
defines ifinit,ifsend,
ifrcv,ifclose
OSAL/BSP ?
Configuration 1:
with IP, w/o SOIS
defines socket,sendto,
recvfrom
OS
defines socket,sendto,
recvfrom
Configuration 3:
w/o IP, w SOIS
Configuration 2:
with IP & SOIS
SOIS
defines SOIS
API’s
ethernet
Fragmentation
Code
SOIS
defines SOIS
API’s
ethernet
Buffer Mgmnt/
Msg Queueing
defines ifinit,ifsend,
ifrcv,ifclose
OSAL/BSP ?
defines ifinit,ifsend,
ifrcv,ifclose
OSAL/BSP ?
Buffer Mgmnt/
Msg Queueing
To Network
To Network
To Network
To Network
Configuration 4:
w/o IP, w SOIS
SOIS
defines SOIS
API’s
ethernet
Fragmentation
Code
defines ifinit,ifsend,
ifrcv,ifclose
OSAL/BSP ?
Buffer Mgmnt/
Msg Queueing
To Ethernet
spacewire
To Spacewire
1553
To 1553
Abstracted
SBN
calls ifinit,ifsend,
ifrcv,ifclose & SB API’s
Abstracted
SBN
calls ifinit,ifsend,
ifrcv,ifclose & SB API’s
Abstracted
SBN
calls ifinit,ifsend,
ifrcv,ifclose & SB API’s
Abstracted
SBN
calls ifinit,ifsend,
ifrcv,ifclose & SB API’s
This diagram was used in the September presentation
of the SBN plan for action. Is it listed here for reference
only.
Notes: This slide shows the different configurations that we might have. It might make sense to develop these configurations from left to right since they kind of grow in that direction.
The left most column shows what we had for our demo. We were using UDP/IP and SBN was calling the OS functions sendto,recvfrom and socket directly.
Configuration #1 shows the same as what we had in the demo except that the SBN in this configuration is abstracted. The OSAL or BSP would define the functions that SBN would call. These functions are show on slide 7.
Configuration #2 uses the SOIS module instead of the OS supplied drivers. This configuration uses UDP/IP and contains support for QOS by way of the SOIS module. Greg and I talked a few times. I got a lot of ideas from him. He made me realize that when SOIS is used, we need this extra block to handle buffer management and msg queuing.
Configuration #3 is a little more complex in that it needs some fragmentation code since IP is not being used.
And configuration #4 shows multiple drivers within the SOIS module.
We can’t push the responsibility of configuring the system onto the mission because these layers need to be included in the cFE object file.